## Slide 1
Without Pretension

## Slide 2
Open HyperMesh and prepare your model.
Make sure that spaces are removed from the names of all the entities.

## Slide 3
Go to File -> Run -> Tcl/Tk Script to run a script to pull the entity information from HyperMesh.

## Slide 4
Select the entity_export.tcl file and run it.

## Slide 5
On successful execution of this script, a pop-up window will appear stating that the operation was successful.

## Slide 6
Start the tool by executing the enclosed .exe file.

## Slide 7
Fill the first text box with the path where the excel file has to be generated.
You can enter the path manually or use the ‘Browse’ button near the textbox.

## Slide 8
Fill the second text box with the path where the TCL file has to be saved.
You can enter the path manually or use the ‘Browse’ button near the textbox.

## Slide 9
Leave the SPC ID text box empty if no Pretension is present in the model.

## Slide 10
If NLPARM (LGDISP) is needed for non-linear analysis, tick this check box.

## Slide 11
Click on the “Generate Excel Workbook” button to generate the Excel sheets at the specified path.

## Slide 12
The generated workbook has two sheets.
The first one is used to generate LOADADD cards.
The second one is used to generate LOADSTEPS

## Slide 13
Names and IDs of loads
Auto-filled from
exported entity information
Fill the name
of the new LOADADDs
Fill the scaling factor
for each load collector

## Slide 14
Auto-filled from the
LOADADD sheet
Fill the name
of the load steps
Input 1 for the selected
load collectors
Select the type of analysis and pretension from the drop-down menu
Note: The 1s input in the selection are binary; it doesn’t imply scaling factors.

## Slide 15
After filling the Excel sheets with the required data, save the workbook and click on the Continue button in the tool.
On successful execution of the program, a pop-up window stating the successful generation of TCL script will appear.

## Slide 16
Run the generated TCL script in HyperMesh.
LOADADD cards and load steps will be created automatically in HyperMesh.
NLPARM card will also be generated; it will be linked to non-linear load steps, if any.
The created entities are highlighted.
Note: New NLPARM card will not be created if NLPARM is already present in the model with the same name.